XD2031 Firmware Architecture Overview
Firmware
main
IEEE
Device
(device)/
ieeehw
ieee
bus
channel
Provider
API
and
Registry
(incl.
Wireformat,
packet)
serial
(arch)/
uarthw
PC
Server
IEC
Device
(device)/
iechw
iec
cmd
TCP/
IP
(device)/
ethhw
wire
fmt
Inter
net
direct
file
SD
Card
sd
card
(device)/
sdhw
FAT
FS
D64

---
Notes:
- Architecture principle is strict separation of concerns, also implementation hiding where useful (e.g. provider API)
- Orange boxes are already implemented, blue ones with dashed lines are possible, if not already planned
- Arrows show the calling direction, so in the main loop the main module calls ieee, and that calls bus, and so on
- Execution is pseudo-asynchronous. So when cmd and file have to wait for a return, they call a main delay loop, which in turn calls the maintenance tasks until a response arrives. The response is noted by a callback given to provider in the send call.
- Hardware-related stuff is separated into hw-independent and hw-dependent (with hw appended) stuff, which is in general located in the device or arch subdirectories
- Main also initializes all modules (which isn't shown here)
- Modules not shown: name, errormsg are helpers for file, cmd; The term module is used as logger and sends log messages via serial

---
Modules:
- ieee – IEEE488 low level handling, i.e. fiddling with “ndaclo()” etc calls. Ieeehw is the implementation of these methods
- bus – high level IEEE/IEC bus handling. Gets received bytes from ieee and interprets them as data, or commands like TALK. It calls the cmd and file (open) modules, and communicates data from and to the data channels
- channel – data transfer between bus and the providers
- file – handles file open for data files
- cmd – handles drive commands
- provider – this is a registry and API for channel, bus and cmd to call the correct back end endpoint. Currently only a serial module exists, but others are planned. Includes “wireformat” and “packet” sub-modules as part of the API
- serial – provider to use the PC Server via UART (via USB) as backend endpoint

---
Future plans:
- iec – IEC bus module for the serial IEC bus (may or may not be with speeder support)
- SD Card support, to allow using an SD card (e.g. on the 15 pin D-Sub connector on the XS1541) as file storage
- Ethernet support – either for connecting the PC Server via TCP/IP or directly
- Maybe D64 support for D64 files on the SD Card