XD2031 Firmware Architecture Overview
Firmware
main
IEEE
Device
(device)/
ieeehw
ieee
bus
channel
Provider
API
and
Registry
(incl.
Wireformat,
packet)
serial
(arch)/
uarthw
PC
Server
file
IEC
Device
(device)/
iechw
iec
TCP/
IP
(device)/
ethhw
wire
fmt
Inter
net
cmd
direct
test
runner
(device)/
sock488
direct
SD
Card
sd
card
(device)/
sdhw
FAT
FS
buffer
D64
relfile

---
Notes:
- Architecture principle is strict separation of concerns, also implementation hiding where useful (e.g. provider API)
- Orange boxes are already implemented, blue ones with dashed lines are possible, if not already planned
- Arrows show the calling direction, so in the main loop the main module calls ieee, and that calls bus, and so on
- Execution is pseudo-asynchronous. So when cmd and file have to wait for a return, they call a main delay loop, which in turn calls the maintenance tasks until a response arrives. The response is noted by a callback given to provider in the send call.
- Hardware-related stuff is separated into hw-independent and hw-dependent (with “hw” appended to the name) stuff, which is in general located in the device or arch subdirectories
- Main also initializes all modules (which isn't shown here)
- Modules not shown: name, errormsg are helpers for file, cmd; The term module is used as logger and sends log messages via serial

---
Modules:
- Ieee/iec – IEEE488 or IEC low level handling, i.e. fiddling with “ndaclo()” etc calls. ieeehw is the implementation of these methods; similar for iec.
- bus – high level IEEE/IEC bus handling. Gets received bytes from ieee and interprets them as data, or commands like TALK. It calls the cmd and file (open) modules, and communicates data from and to the data channels
- channel – data transfer between bus and the providers
- file – handles file open for data files
- cmd – handles drive commands
- provider – this is a registry and API for channel, bus and cmd to call the correct back end endpoint. Currently only a serial module and a FAT fs for SD cards exists, but others are planned. Includes “wireformat” and “packet” sub-modules as part of the API
- direct – a provider for direct access file handling (B-*, U1/U2)
- relfile – a provider for handling of relative files
- buffer – drive buffer handling, used by relfiles and direct access files
- serial – provider to use the PC Server via UART (via USB) as backend endpoint

---
XD2031 Initialization
Initialization from the PC side:
- You can override the EEPROM configuration with command line parameters on the pc server
- The parameters are sent to the device when the pcserver starts
- When the device gets reset, it sends a notification to the pcserver, that then re-sends the configuration.
- The parameter channel simply forwards “X” drive commands from the pcserver to the device; however, they are bus-specific. Thus the command line is:
  - -X<device>:<command>
  - -Xiec:U=9
- When received by the serial module, it is forwarded to the bus module, which selects the bus and sends the command there

---
Future plans:
- SD Card support, to allow using an SD card (e.g. on the 15 pin D-Sub connector on the XS1541) as file storage
- Ethernet support – either for connecting the PC Server via TCP/IP or directly
- Maybe D64 support for D64 files on the SD Card