XD2031 Server Architecture Overview
pcserver (fsser)
main
fscmd
(dispatcher)
Provider
API
and
Registry
fs
PC
files
resolver
(handler.c)
disk
images
TCP/
IP
Serial
device
Serial
device
tcp
To the providers
Resp. handlers
Via open files or
Registered
endpoints
FTP
curl
socket
device
Unix
socket
zip
handler
API
and
Registry
HTTP
PRG
handler
channel
x00
handler

---
Notes:
- Architecture principle is strict separation of concerns, also implementation hiding where useful (e.g. provider API)
- Orange boxes are already implemented, blue ones with dashed lines are possible, if not already planned
- Arrows show the calling direction, so in the main loop the main module calls ieee, and that calls bus, and so on
- Main also initializes all modules (which isn't shown here)
- Modules not shown: diskimg for disk image handling; mem, types and registry are general helpers; xcmd handles the -X command line options; the log module provides log output

---
Modules:
- Serial and socket handle the initialisation of the serial or socket device respectively
- fscmd is the main command dispatcher; it receives wire packets and handles them
- resolver: resolves paths and file names. Recursively goes through the directory levels, looking for matching handlers and providers
- provider: registry for the providers. Also handles charset conversion for providers
- handler: registry for the file type handlers
- fs, di, tcp, curl: current set of providers
- x00: currently available handler (for Pxx, Rxx, … files)

---
XD2031 Initialization
Initialization:
- The server takes a number of parameters.
- With the “A” assign parameter, you can assign paths to the drive numbers, like
  - -A0:fs=/foo/bar/path
  - -A1:tcp=localhost
- The parameter channel simply forwards “X” drive commands from the pcserver to the device; however, they are bus-specific. Thus the command line is:
  - -X<device>:<command>
  - -Xiec:U=9

---
Future plans:
- Further code cleanup
- More file type handlers