Init after ATN, clear DAV, EOI, DATA
ATNIRQ:
   LDX #$FF ; CLEAR STACK
   STX cmdnum
   TXS
   LDA io_ifr? ; CLEAR IRQ FLAG
   LDA #$18 ; DAVO+EOIO
   ORA io_ieee_ctl ; FREE CONTROL LINES
   STA io_ieee_ctl
   LDA #$FF
   STA io_ieee_data_out ; FREE DATA LINES
Set ATNA, NRFD HI, NDAC LO
ATN10:
   LDA #$7 ; DACO+RFDO+ATNA
   ORA io_ieee_ctl
   STA io_ieee_ctl
Wait DAV low or ATN HI
ATN20:
   BIT io_ieee_ctl
   BVC ATN30 ; DAV LO -> ATN30
   BMI ATN20 ; ATN LO -> ATN20 (wait loop)
   BPL ATN50 ; ATN HI -> ATN50
LISTEN loop
LISTEN:
   ; NRFD HI
   LDA #$4 ; RFDO
   ORA io_ieee_ctl
   STA io_ieee_ctl
   ; Wait DAV LO – ATN exits to IRQ
LSN10:
   BIT io_ieee_ctl ; DAV: LO
   BVS LSN10
   ; Find channel
   JSR fndwch ; WAS LDX SA
   BCS LSN15
   LDA chnrdy,X
   ROR A ; OK, OPEN FOR LISTEN
   BCS LSN30
LSN15:
   LDA orgsa ; WAS TXA
   AND #$F0 ; SA=OPEN?
   CMP #$F0
   BEQ LSN30
LSN20:
   LDA sa
   CMP #$1
   BEQ LSN25
DAV LO → NRFD LO, Read data, NDAC HI
ATN30:
   LDA #$FB ; NRFD LO
   AND io_ieee_ctl
   STA io_ieee_ctl
   AND #$20 ; EOIFLG
   STA eoiflg ; SAVE EOI
   LDA io_ieee_data_in
   EOR #$FF
   STA data ; SAVE COMMAND
   LDA #$FD ; NDAC HI
   AND io_ieee_ctl
   STA io_ieee_ctl
ATN HI – Check LISTEN
ATN50:
   LDA lsnact
   BEQ ATN60	; (to talk)
   ; Set ATNA and set NRFD LO
   LDA #$FA ; 255-RFDO-ATNA
   AND io_ieee_ctl
   STA io_ieee_ctl
   CLI
   JSR LISTEN
   JMP idle
Switch on received ATN command
DCDE:
   LDY #$0
   LDA data
   AND #$60
   CMP #$40 ; TALK?
   BEQ DCDE60
   CMP #$20 ; LISTEN?
   BEQ DCDE20
   CMP #$60 ; SECONDARY?
   BEQ DCDE70
   BNE DCDE80	; OTHER
ignore rest of data
   ; Wait for DAV hi
LSN21:
   BIT io_ieee_ctl
   BVC LC6FE ; LSN21
   ; NDAC HI
   LDA #$FD ; 255-DACO
   AND io_ieee_ctl
   STA io_ieee_ctl
   ; return from Listen (timeout in host)
   RTS
Save (secaddr == 1)
   ; read and drop data if channel not open
LSN25:
   ; NRFD LO
   LDA #$FB ; 255-RDFO - ACCEPT ALL DATA
   AND io_ieee_ctl
   STA io_ieee_ctl
   ; NDAC HI
   LDA #$FD ; 255-DACO
   AND io_ieee_ctl
   STA io_ieee_ctl
   ; Wait for DAV Hi
LSN26:
   BIT io_ieee_ctl ; DAV HI
   BVC LSN26
   ; NDAC LO
   LDA #$2 ; DACO
   ORA io_ieee_ctl ; DAC LO
   STA io_ieee_ctl
   ; NRFD HI
   LDA #$4 ; RFD HI
   ORA io_ieee_ctl
   STA io_ieee_ctl
   ; Wait for DAV HI
LSN28:
   BIT io_ieee_ctl ; WAIT DAV LO
   BVC LSN28
   JMP LSN25	; DO UNTIL ATN PULLED
Found open channel
LSN30:
   ; NRFD LO
   LDA #$FB ; 255-RFDO
   AND io_ieee_ctl
   STA io_ieee_ctl
   ; store data
   AND #$20 ; EOI
   STA eoiflg
   LDA io_ieee_data_in
   EOR #$FF
   STA data
   SEI
   ; NDAC HI
   LDA #$FD ; 255-DACO
   AND io_ieee_ctl
   STA io_ieee_ctl
LSN40:
   ; Wait DAV HI
   BIT io_ieee_ctl
   BVC LSN40
   ; NDAC Lo
   LDA #$2 ; DACO
   ORA io_ieee_ctl
   STA io_ieee_ctl
   JSR put
LSTRTN:
   CLI
   JMP LISTEN
Process TALK address
DCDE60:
   STY tlkact
   LDA data
   CMP tlkadr
   BNE DCDE30
   STA tlkact
   STY lsnact
   BEQ DCDE50	; always
Process SECONDARY address
DCDE70:
   LDA lsntlk? ; ADRSED
   BEQ DCDE80 ; NOT ADDRESSED
   LDA data
   STA orgsa
   PHA
   AND #$F
   STA sa
   PLA
   AND #$F0 ; CLOSE?
   CMP #$E0
   BNE DCDE80
   JSR close
Process LISTEN address
DCDE20:
   LDA data
   CMP lsnadr
   BEQ DCDE40	; MY LISTEN ADDRESS
   CMP #$3F ; UNLSN
   BNE DCDE30
   STY lsnact
DCDE30:
   STY lsntlk? ; ADRSED - NOT PRIMARY ADDRSED
   JMP DCDE80
DCDE40:
   STA lsnact
   STY tlkact
ATN HI – Check TALK
ATN60:
   ; Set ATNA and set NDAC HI
   LDA #$FC ; 255-ANTA-DACO
   AND io_ieee_ctl
   STA io_ieee_ctl
   LDA tlkact
   BEQ ATN70
   CLI
   JSR TALK
   atn110:
ANT70
   JMP idle
TALK loop
TALK:
   JSR fndrch
   BCS NOTLK	; TEST IF CHANNEL READY
TALK1:
   LDX lindx
   LDA chnrdy,X
   BMI tlk05 ; TLK10
NOTLK:
   RTS
TLK10:
   ; Wait NRFD HI
   BIT io_dskcnt ; RFD: HI
   BPL TLK10
   ; Put data on bus
   LDA chndat,X
   EOR #$FF
   STA io_ieee_data_out
   ; put EOI on bus, set DAV
   LDA chnrdy,X
   ORA #$E7 ; 255-EOIO-DAVO
   AND io_ieee_ctl
   STA io_ieee_ctl
   ; Wait NRFD LO, bus error on NDAC HI
TLK20:
   BIT io_dskcnt
   BPL TLK30	; NRFD is Low → end
   BVC TLK20	; NDAC is Low → loop
   ; end of transmission
   ; DAV & EOI HI
   LDA #$18 ; DAVO+EOIO
   ORA io_ieee_ctl
   STA io_ieee_ctl
   JMP idle
   ; get next data
TLK30:
   JSR LDA84 ; GET
   ; Wait for NDAC Hi
TLK35:
   BIT io_dskcnt
   BVC TLK35
   ; Clear bus
   LDA #$FF
   STA io_ieee_data_out
   ; Clear DAV & EOI
   LDA #$18 ; DAVO+EOIO
   ORA io_ieee_ctl
   STA io_ieee_ctl
   ; Wait NDAC Low
TLK40:
   BIT io_dskcnt
   BVS TLK40
   BVC TALK1	; always
End TALK/LISTEN address
DCDE50:
   LDA #$20
   STA sa ; DEFAULT SA
   STA orgsa
   STA lsntlk? ; ADRSED - PRIMARY ADDRESSED
   BNE DCDE80	; always
Wait end of DAV
DCDE80:
ATN40:
   BIT io_ieee_ctl
   BVC ATN40
   JMP ATN10